## Slide 1
Project: Automated on-line monitoring system of incoming ore flows for mining and processing plants
Almaty 2017
Senior Scientist Grant Program Manual

## Slide 2
General information
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Project Leader – Doctor of Technical Sciences, U. Tukeyev
Grant recipient–«TST-16» LLP
Business partner – Systemotechnika LLP
Sub-project: Automated on-line monitoring system of incoming ore flows for mining and processing plants
Notes: Рисунок 4

## Slide 3
Automated on-line monitoring system of incoming ore flows for mining and processing plants
PROBLEM: MANAGEMENT’S EFFICIENCY FOR MULTI-FLOW ORE ENRICHMENT SYSTEM
The practical operational technology for measuring the quality of processed ore is oriented at fine-fraction ore flows and are used in a single-flow scheme of ores supply for enrichment.
However, single-flow ore supply scheme does not provide the maximum loading of enrichment plants equipment.
At multi-flow ore supply scheme, fine-fractioned ore flows are obtained after crushing when it is hard to distinguish in a ore flow which ore comes from a certain mine.
Thus, there is a problem: prior to crushing it is hard to quickly measure the quality of ore from pits, and after crushing it is hard to distinguish which ore came from a certain mine.
This problem of operational monitoring of input ore flows at multi-flow ore supply scheme for enrichment has still not been resolved.
Notes: Рисунок 4

## Slide 4
Automated on-line monitoring system of incoming ore flows for mining and processing plants
THE PROPOSED TECHNOLOGY
The essence of technology is considering temporal dependencies of discrete flows of ores wagons from different quarries in the mixed output flow of the crushing shop.
Measuring of quality of fine-fraction ore flow at crushing shop takes place.
Then back in time (temporal) projecting of measured quality of ore into discrete flows of wagons from the quarries takes place.
That is how the real-time identification of the quality of wagon ores of certain quarries takes place.
Notes: Рисунок 4

## Slide 5
Конвейер
Конвейер
Objects of monitoring
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 6
Receiving ore from the mines to the dressing plant (DP). Positioning of the formulations in the unloading zone
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Analyzer
Scales
Semaphores
Notes: Рисунок 4

## Slide 7
Receiving ore from the mines to the dressing plant. Unloading into the hoppers of mills
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Scales
Analyzer
Analyzer
Scales
Dump to the hopper 1
Dump to the hopper 2

## Slide 8
Analytics block: Disintegration of the flow of ore mixture after large crushing plant (LCP) on the basis of belonging to ore mines
Chronology ore carriers arriving at the factory
Quality control and dynamics of the ore flow after the LCP
The block of the account of quality and volume of ore accepted on LCP
Temporal pattern of movement in the unloading area
Temporal pattern of work flow transport system
of the LCP
Technological scheme of the monitoring object
Chronology of movement in the unloading area
Unloading area
Mine
Analyzer
Scales
Summary results of the operational monitoring of the inlet ore flows of DP
Structural scheme of information gathering and formation of the operational report of monitoring
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Notes: Рисунок 4

## Slide 9
Advantages of the proposed technology
Automated on-line monitoring system of incoming ore flows for mining and processing plants
The time for determining the quality of ores from mines is reduced: traditional two or three days are reduced to real time, i.e. to the rate of the technological process.
Operational management of the mine - crushing - enrichment processing chain is ensured.
A real informational basis is created for objective self-supporting relationships between the mining and beneficiation

## Slide 10
Work plan for the first half of 2017
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Works | 1 quarter | 2 Quarter | 3 quarter | 4 quarter
Specification of methodological and scientific and technical solutions |  |  |  | 
Development of system-wide solutions |  |  |  | 
Development of technical support |  |  |  | 
Development of technical support |  |  |  | 
Development of information support |  |  |  | 
Development of application software |  |  |  | 
Correction of system-wide solutions (structure and functions) |  |  |  | 
Correcting the system platform |  |  |  | 
Justification of the choice of measuring equipment |  |  |  | 

## Slide 11
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Results of works for the first half of 2017
Works | QUARTER |  | Status | RESULTS
 | 1 | 2 |  | 
Specification of methodological and scientific and technical solutions |  |  | Done 100% | Engineering solutions for calibration of measuring channels and parameters of the analytical subsystem
Development of system-wide solutions |  |  | Done 100% | Decisions on the structure, composition and communications of AS OMIOQ
Development of technical support (TS) |  |  | Done 70% | TS for the level of basic automation (Controller),
Development of mathematical support (MS) |  |  | Done 40% | Models and algorithms of subsystems for data collection and situational analysis
Development of information support (IS) |  |  | Done 100% | Information models describing processes at monitoring objects
Development of application software |  |  | Done 40% | The application software for the basic automation level (Controller)
Correction of system-wide solutions (structure and functions) |  |  | Done 100% | Adjusted system-wide solutions in terms of the structure and functionality of the AS OMIOQ
Correcting the system platform |  |  |  | There is no in the plan of first half of the year
Justification of the choice of measuring equipment |  |  |  | Technical proposals on the list of analyzers for AS OMIOQ

## Slide 12
Name of events / works | Results
Development of documents regulating the duties of personnel in accordance with the standards of the Republic of Kazakhstan Development of the ISO-2000 document Quality Manual Rent of office premises for TST-16 Purchase of consulting services for the design of AS OMIOQ Reporting and information activities Development of the document "Technology commercialization strategy" | Job descriptions and regulations, internal regulations, collective agreement, employment contracts Quality Manual, Quality Instructions for Project and Commissioning Work Rent of office premises to the address: Almaty, Amangeldy, 40 A tender was held to provide consulting services for LLP TST-16. The results are published on the www.fpip.kz Participation in meetings, presentations, meetings with PMT The document was submitted to the PMU
Activities to ensure the functioning of the project team in the framework of TST-16
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 13
Cost category | Plan | Fact | Explanation of deviation
Salary of employees, total | 11 425 000 | 5 389 980 | Later decision by ISCB on the commencement of work
Equipment | 4 732 000 | - | Later decision by ISCB on the start of work
Laboratory materials and consumables | - | - | 
Traveling expenses | 208 330 | 187 354 | Later decision by ISCB on the start of work
Minor construction works | - | - | 
Recruitment consultants | 8 333 333 | 1 915 000 | Later decision by ISCB on the start of work
Registration of patents and publications | - | - | 
Training, seminars | - | - | 
Services of third-party organizations and individuals | - | - | 
Overhead and other expenses | 2 803 333 | 910 165 | In connection with the late start of work
TOTAL | 27 501 996 | 8 402 499 | 
Financial report of grant funds (from 30.11.2016 to 01.06.2017) in tenge, KZT
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 14
Payment Category / Subcategory | Contractor, number and date of contract | Contract value | Current payment | Balance
Overhead / Rent of Premises | LLP “AVA-Stroysystema", lease agreement No. 0/02-2017TST of 08.02.2017 | 2 790 000 | 837 000 | 1 953 000
Consulting services | LLP "SKADA LTD", contract No. 01/05-17TCT of 19/05/ 2017 | 19 150 000 | 1 915 000 | 17 235 000
TOTAL |  | 21 940 000 | 2 752 000 | 19188000
Procurement report for the first half of 2017 in tenge, KZT
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 15
Technology commercialization strategy. Business model
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 16: Automated on-line monitoring system of incoming ore flows for mining and processing plants
Specification of methodological and scientific-technical solutions for the creation of the OMIOQ "Timed Interval Calculus" Technology
Rules for the TIC-model of belonging the ore of the segment of output stream to a particular wagon of one of the input discrete streams, and hence the definition of ore belonging to a career
Rule 1. Binding events to the timeline. If Sisv=true then Tisv = t , where: Sisv – sign of the dump of the i-th wagon, Tisv - dump time of the i-th wagon, t – current time. This rule means that if an accident occurred in the wagon, the time for the wagon is equal to the current time.
Rule 2. Determination of the time interval for crushing ore in a bunker. If 〖 Wioj – Pbunk ≠ 0〗 ={x,y: T ¦ ∀t : [x…y] ∗(Wi(α([x…y])) = Wioj ⋀ Wi(ω ([x…y]))=0 ⋀ Wi= Wi- Pbunk)} then tbunk= σ([x…y]), where: Wioj – estimated weight of the ore of the i-th wagon; Pbunk - Hopper capacity per second; Wi – Current weight of the ore of the i-th wagon, tbunk - The time interval for crushing the ore of the bunker. This rule means that in each cycle (1 second) of the total weight of the ore in the bunker, the quantity equal to the productivity of the hopper per second is subtracted. This rule allows you to calculate the time spent by the bunker on crushing the dumped car and fix the expected moment of the end of the wagon exit from the bunker..
Rule 3. Determination of the time interval from the moment of appearance of the ore of the wagon on the conveyor until the moment of measurement on the conveyor scales. tikonv=Lkonv/Vkonv, where Lkonv – Conveyor length to conveyor weights; Vkonv – Conveyor speed.
Rule 4. Determination of the expected time of the beginning of the flow of ore in the wagon through the balance.. Tiojnach = Tisv + tbunk + tikonv. This rule means that the expected time for the beginning of the flow of ore in the wagon through the scale is determined by the sum of the time of the dump of the wagon with the time interval for crushing the ore of the hopper and the time interval when the appearance of the ore of the wagon on the conveyor.

## Slide 17: Automated on-line monitoring system of incoming ore flows for mining and processing plants
Specification of methodological and scientific-technical solutions for the creation of the OMIOQ "Timed Interval Calculus" Technology. Continuation
Rules for the TIC-model of belonging the ore of the segment of output stream to a particular wagon of one of the input discrete streams, and hence the definition of ore belonging to a career
Rule 5. Calculation of the length of the time interval of the wagon's flow. If 〖Sisv=true & t ≥ Tiojnach〗 = {x,y : T ¦ ∀t : [x…y] ∗( Sisv=true ⋀ t ≥ Tiojnach)} then { Wi∑=0; while (Wi∑ ≤ Wioj) Wi∑ = Wi∑ + Wi; t=t+1; end {Tiint = t - Tiojnach; Tiojkon = Tiojnach + Tiint}} This rule means that if the wagon wreck event occurred and the current time is greater than or equal to the time of the expected start of the wagon unloading, then the condition is checked whether the total weight of the wagon wagon is less than the expected weight of the wagon and, as soon as this condition is not fulfilled, calculated the interval of ore flow of wagon and time of the end of the wagon flow.
Rule 6. Correction rule of the time beginning of the flow of the wagon. If 〖W(t)-W(α)≥0,05W(α)〗={ x,y : T ¦ ∀t : [x…y] ∗ (W(t)-W(α([x…y]))) ≥0,05 W(α([x…y]))⋀σ[x…y]≥5} then tinachpot=α([x…y]). This rule means that as the start time of the flow, the system captures a significant (more than 5 seconds) and stable (more than 5%) increase in the signal from the weight sensor.
Rule 7. The rule for adjusting the end time of the wagon's flow. If 〖W(t)-W(α) ≤0,03W(α)〗={ x,y : T ¦ ∀t : [x…y] ∗ (W(t)-W(α([x…y]))) ≤ 0,03W(α([x…y])) ⋀ σ[x…y]≥5} then tikonpot = w([x…y]). This rule means that as the end-of-flow time the system fixes a stable (more than 5 seconds), close to zero (not more than 3%) value of the signal from the weight sensor.

## Slide 18
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Specification of methodological and scientific-technical solutions for the creation of the OMIOQ
The main refinements of the technique of operational diagnostics of input ore flow characteristics
1. Refinement of the calibration procedure for the measuring channels for the AS OMIOQ The need for refinement. Methodical solutions for calibration of measuring channels are predetermined by the need to take into account changes in the metrological characteristics of instruments used in the AS OMKVR due to their mechanical wear or changes in the electromagnetic environment in the measurement zone. In the basic functional specifications of the AS OMIOQ, the channel calibration service is not taken into account.
2. Solutions for adjusting the parameters of the mathematical model of monitoring in the AS OMIOQ The need for refinement. In the basic functional specifications of the OMIOQ, the inevitable changes in the parameters of objects and monitoring processes during operation were not taken into account, which requires periodic adjustment of the characteristics of the instruments and adaptation of the model parameters as the residuals arise between the model and real indicators. The mathematical model forms the basis for the procedure for projecting the dynamics and chronology of unloading wagons into a bunker to segments of ore flow after a major crushing operation. Inaccuracies in the parameters of the model will reduce the objectivity of the results obtained.

## Slide 19
AS OMIOQ
Analytical unit of the AS OMVKR
Reference train
For a standard train, for each wagon before unloading, the following was determined in the hopper: the weight of the ore, the content of the useful component, the mine and the like
Monitoring data
Reference data
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Specification of methodological and scientific-technical solutions for the creation of the OMIOQ
Adjusting model parameters
Adjustment of the parameters of the analytical block of AS OMIOQ based on the use of a simulation model of processes at monitoring objects
Adjusted parameters of the analytical block

## Slide 20
Lack of ore flow on the conveyor
W
ti
t
t2
t1
t1
t2
Calibration of measuring devices is carried out in the absence of ore on a moving conveyor.(In this example, on the intervals t1, t2, ti).
For zero is the value (Wt1+Wt2+……+ Wti)/ (t1+t2+…+ti)
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Specification of methodological and scientific-technical solutions for the creation of the OMIOQ Calibration of measuring instruments

## Slide 21
Justification of the choice of analyzers
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Parameters | Instruments with X-ray tube | Radioisotope | Laser | Neutron | Optical
Analyzed elements | From Al to U | From Mg to U | From C to U | From C to U | From H to Mt
Value Range Ambient temperature Air, oC | -20 to +45 | -30 to +50 | -20 to +45 | -30 to +50 | 
Dimensions, mm | 890x275x240 | Sensor 150х140х300 Power cabinet 300х250х170 | 1500x800x1300 | 2103х1690х1575 | Lighting unit 2000x2000x1000 Cabinet with electronics 1300х800х200
Weight, kg | 45 | Sensor 5 Power cabinet 6,5 | 450 | from 2721 to 4081 | 180
Area / volume of analysis | Surface | Scope | Surface | Scope | Surface
Limits of detection and accuracy | For all stream analyzers - up to 100ppm (0.01%), vary depending on the elements |  |  |  | 
Danger to health Of staff | there is | Unlikely | no | there is | no
Frequency of analysis, samples / min | Continuously | Continuously | 3-20 | 1, Possibly continuously | 20

## Slide 22
Project technical support. Structural diagram of the Hardware Complex
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 23
Technical support project. Instrumentation
Automated on-line monitoring system of incoming ore flows for mining and processing plants
Индукционный конвейерный анализатор МВ-5
Конвейерный анализатор наличия Fe в потоке
Notes: РИСУНОК 2

## Slide 24
Technical support project. Cabinets (General drawing)
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 25
DATABASE
PLC
АРМ
Data on ore flows After crushing Once every 10 seconds
Chronology of unloading Once a second
Situational information by unloading zone By event
Unloading control On request
Information Support. Data collection scheme for analysis
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 26
DB_ПУТЬ
Номер пути Номер склада
DB_СКЛАД
Номер склада
Скорость дробления
DB_ВЕРТУШКА
Номер вертушки
Номер склада
DB_СВАЛ
Номер вертушки
Номер вагона
DB_ВАГОН
Номер вертушки
Номер вагона
DB_ВЕСЫ
Номер вагона
ВЕС
DB_БУНКЕР
Номер вагона
DB_СВОДКА
Номер вагона
Номер вертушки
Номер склада
Номер пути
Information Support. Logical diagram of the database of the controller station
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 27
DB numbers | Characteristics of ore flow / Situational information | Fixing / calculation frequency | Duration of storage | Note
DB51 – DB58 | Instantaneous weight and quality value from sensors on the conveyor | 1 second | two shifts | One DB for each indicator of each queue
DB140 – DB141, DB146 – DB149 | Moments of the input / output of the turntable for unloading, moments of movement / shutdown of the turntable, moments of the wagon | 1 second | two shifts | One DB for each indicator
DB301 – DB1091 | Weighted average weight and quality value for each wagon of the unloaded train | Every second calculation for the time of unloading the turntable | two shifts | The number of DBs is set on the basis of the maximum number of wagon trailers unloaded in two shifts
DB301 – DB1091 | Weighted average weight and quality value for each wagon of the unloaded train in one hopper | Every second calculation for the time of unloading the turntable | two shifts | 
Information Support. Functionality DB of the controller station
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 28
№ DB след-го вагона =5 № DB пред-го вагона =0
DB3 Вагон №1
№ DB предыдущей вертушки = 0
DB3 Вертушка №1
№ DB предыдущей вертушки = 3
DB5 Вертушка №2
№ DB предыдущей вертушки = 5
DB6 Вертушка №3
№ DB предыдущей вертушки = {k}
DB{N} Вертушка №S
№ DB предыдущей вертушки = {N}
DB{M} Вертушка №S+1
№ DB след-го вагона =6 № DB пред-го вагона =3
DB5 Вагон №2
№ DB след-го вагона ={K} № DB пред-го вагона =5
DB6 Вагон №3
№ DB след-го вагона ={M} № DB пред-го вагона ={J}
DB{N} Вагон №S
№ DB след-го вагона =0 № DB пред-го вагона ={N}
DB{M} Вагон №S+1
№ DB след-го вагона вертушки=5
DB3 Вагон №1
№ DB след-го вагона вертушки=7
DB4 Вагон №1
№ DB след-го вагона вертушки={K}
DB7 Вагон №1
№ DB след-го вагона вертушки={M}
DB{N} Вагон №{S}
№ DB след-го вагона вертушки=0
DB{M} Вагон №S+1
…………………………...........
Information Support. Linked lists of data blocks (DB)
Automated on-line monitoring system of incoming ore flows for mining and processing plants
…………………………...........
…………………………..........
Linked list
«Вертушки»
Linked list
«Вагоны очереди»
Linked list
«Вагоны вертушки»

## Slide 29
DB «Путь»
1. № пути
2. № DB последней вошедшей вертушки
3. Момент Команды на ввод данных по вертушке
4. Момент Команды на объединение вертушек
5. Момент Команда на разделение вертушки
6. № вертушки (для команд)
7. № электровоза (для команд)
8. № склада (для команд)
9. Вес вертушки заявленный (для команд)
10. № вертушки для объединения
11. Количество вагонов в первой вертушке при разделении одной вертушки на две
DB «Вагон»
1. Тип (обмоторенный / обычный)
2. Заявленная масса
3. Содержание Fe
4. Время свала
5. Время начала выхода из бункера
6. Время конца выхода из бункера
7. Время начала прохода весов
8. Время конца прохода через весы
9. Ссылка DB вертушки
10. Номер вагона
11. Ссылка DB след. вагона вертушки
12. Ссылка DB след. сваленного вагона
13. Ссылка DB пред. сваленного вагона
DB «Бункер»
1. Емкость
2. Текущая масса
3. Коэфф. коррекции производительности
4. Производительность на выходе
5. DB первого вагона
6. DB последнего вагона
DB «Весы»
1. Текущий вес без нуля
2. Текущий вес с учетом нуля
3. Ноль весов
4. Суммарный вес текущего потока
5. Ссылка DB текущего вагона
6. Время начала потока
7. Время конца потока
8. Флаг конца потока
9. Магнитная восприимчивость
DB «Сводка»
1. Порядковый номер строки сводки
2. Время подачи вертушки на бункерный путь
3. Время выхода вертушки с бункерного пути
4. Номер электровоза
5. Номер склада, с которого загружена вертушка
6. Вес вертушки заявленный (введенный оператором ККД)
7. Вес вертушки, реально принятый на фабричный передел
8. Средне взвешенное содержание железа в руде вертушки
9. Количество выгруженных вагонов
10. Номер бункерного пути, на котором находится вертушка
DB «Склад»
1. Номер склада
2. Формула Коэффициент «А»
3. Формула Коэффициент «B»
4. Скорость прохождения руды через дробилку
Database table structure
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 30
Mathematical support. Algorithms
Automated on-line monitoring system of incoming ore flows for mining and processing plants

## Slide 31
Automated on-line monitoring system of incoming ore flows for mining and processing plants
The main areas of work for the establishment of the OMVCS in the second half of 2017
First half of the year The work of the first half of 2017 was carried out in accordance with the subproject implementation plan
Second half of the year The works of the second half of 2017 are planned for implementation in accordance with the subproject implementation plan and include:
Completion of design work for: maintenance; Mathematical support; Applied software of AS OMVKR.
Completion and installation of cabinet structures.
Completion of the system software platform.
Autonomous adjustment of control stations and workstations in polygon conditions of "TST-16" LLP.